## Slide 1: Learning what airlines actually prefer
Every flight-plan revision records a choice the airline made — this
is what those choices reveal
EUROCONTROL Innovation Hub · Maastricht Upper Area Control Centre

## Slide 2: The goal: proposals airlines will actually accept
01 A cheaper route is not enough — If the airline would not have chosen it, the proposal is ignored
02 The system must learn preference — Not just minimise fuel or time, but predict which route this airline would accept
03 Preference is learned, not assumed — From what airlines have actually chosen before, not from a cost formula
An ignored proposal channel is a channel that eventually gets switched off.

## Slide 3: Pairs, not sets
Earlier work compared the filed route to a SET of generated alternatives. This work compares PAIRS from real revisions instead.

## Slide 4: Every revision is a trade
Amsterdam → Barcelona: 39 extra minutes and 1.4 tonnes of fuel to avoid 102 minutes of network delay.

## Slide 5: Not every revision is about delay
No regulation involved — the operator identified a cheaper route and filed it directly.

## Slide 6: What the archive records
Most route changes are routine — not the dramatic cases just shown.

## Slide 7: How a cost rule is tested
01 Take a held-out pair — Two real routes from one revision, never used to train anything
02 Apply the rule — For example, “prefer less fuel” — the rule always picks one of the two routes
03 Compare to what happened — Did the rule's pick match the route the airline actually filed?
04 Accuracy = share correct — Across all such pairs, “prefer less fuel” is right only 44.9% of the time
The same test, repeated for every rule in the next chart — only one beats a coin flip.

## Slide 8: Cost rules score below chance
Simple cost rules all underperform a coin flip. Only “avoid delay” helps.

## Slide 9: How it works, start to finish
Revisions and stay pairs both become training examples. The model learns the pattern and estimates its own confidence.

## Slide 10: Two datasets, two questions
Revision pairs — 884,000 pairs
One flight refiles: it files route A, then switches to route B before departure. The pair is (A, B) — which did the airline pick?
Stay pairs — 6,672 pairs
Two flights, same day, same route choice. One was hit by a regulation, had a real alternative (its twin's route), and stayed. Pair: (kept, declined).
Both feed one model — stay pairs count 10× each to offset being 132× rarer, then held out to test the fix.

## Slide 11: A stay pair, concretely
01 Two flights, same day, same city pair — Same origin, destination, and aircraft type — but different routes
02 One flight was delayed; its twin was not — The twin's route is a real, demonstrated alternative — flown that same day
03 The delayed flight kept its route anyway — Its route is labelled preferred; the twin's route is the declined alternative
04 This happened despite the cost — Across all 6,672 such pairs: median peak delay 31 minutes, and 47.5% kept the pricier route in fuel
Real evidence that operators value stability itself — exactly what an over-eager model would violate.

## Slide 12: How the bias test works
01 Find two similar flights, same day — Same origin, destination, aircraft type — one delayed, one not
02 The delayed flight had a reason to move — Its twin's route was a real, demonstrated alternative — and it stayed anyway
03 Label “stayed” as the preferred route — Delay features are hidden, so route geometry alone must decide
04 Score it without seeing delay — Before this fix, the answer was 45.7% — worse than chance
This is the regulation-blind test behind the next chart — the fix raises this to 57.3%.

## Slide 13: Correcting a bias toward change
With regulation clues hidden, route-only accuracy on stay pairs: 45.7% before correction, 57.3% after.

## Slide 14: Why the model sees differences, not totals
01 Routes in different pairs vary hugely in scale — A short regional hop and a long intercontinental sector burn very different absolute fuel
02 So each indicator is rebased to its own pair — Subtract the pair's minimum from both routes — the cheaper one becomes 0
03 The model sees only the extra, not the total — 0 kg and 300 kg, not 2,000 kg and 2,300 kg — the gap that actually drove the choice
Skip this step, and the next chart shows exactly what it costs.

## Slide 15: The one choice that changes everything
2,000 kg alone is meaningless; the 300 kg gap is everything. Drop it: accuracy falls to chance (60.6% → 50.8%).

## Slide 16: How accuracy and confidence are measured
01 Score both routes in a held-out pair — Never used in training, tuning, or calibration
02 Correct = higher score matches the choice — Accuracy is this, averaged across all pairs: 68.3% overall
03 The score gap is a confidence signal — A bigger gap between the two scores means a more confident call
04 Coverage = share of cases answered — Answering only the surest fifth raises accuracy to 95%
The same measure drives both charts that follow.

## Slide 17: The headline, and the curve behind it
68.3% accuracy across all cases; 95% on the most confident fifth.

## Slide 18: Where the accuracy lives
Accuracy rises with the delay being avoided — the larger the
incentive, the clearer the decision.

## Slide 19: How feature importance is measured
01 Treat each input as a player in a game — Route, fuel, delay, distance, and every other feature
02 The payout is the model's score — For one specific route, on one specific decision
03 Add features one at a time, in random order — Measure how much the score moves each time one joins
04 Average that movement over the quarter — Each feature's fair share of the credit — route structure earns the most
This ranks what moves the score, not what an operator consciously weighs.

## Slide 20: What drives the model’s decisions
Route structure carries more weight than any single cost
indicator — fuel, time, or distance.

## Slide 21: How a score becomes a proposal
01 The model scores each candidate route — The alternative comes out +3.6 ahead — just the model's own number, not yet a percentage
02 History says how sure to be — Among past cases with a lead about this big, the airline picked the model's suggestion 8 times out of 10
03 Only propose if that clears the bar — The policy requires at least 6 of 10; 8 of 10 clears it, and it only counts as confirmed once the airline's later filing agrees
This is the policy behind every fuel figure in this talk.

## Slide 22: The count behind that probability
That's the whole mechanism — real past cases, counted, compared against the bar the policy requires.

## Slide 23: From a score to a decision
More confidence required means fewer suggestions but better precision. At this threshold: 16.4 kt fuel a quarter, ~200 kt CO₂/yr.

## Slide 24: A proposal, concretely
01 Two candidate routes — Same airline, aircraft, and departure time — no delay involved
02 Comparison — One route burns 2,016 kg less fuel — roughly a fifth of trip fuel
03 Confidence check — This case clears the threshold set for an 80%-precision channel
04 Outcome — The airline's later filing matched the suggested route exactly
One case from the test period, followed start to finish.

## Slide 25: Where the value sits
Six of 815 airlines account for half of the confirmed fuel;
28 account for four-fifths.

## Slide 26: How the ageing test works
01 Shift the whole design back one year — Train through October 2025 instead of February 2026
02 Freeze everything at the cutoff — Same threshold, same calibration — no peeking at 2026 data
03 Score month by month, unmodified — January through June 2026, one month at a time
04 Compare to the fresh model on the same months — Isolates pure ageing — precision barely moves, as the next chart shows
The result: precision holds at 77-79% even six months out.

## Slide 27: How fast does the model age?
Precision holds steady (77-79%) six months on; it simply proposes less. Retraining recovers the 1-3 points that drift costs.

## Slide 28: Open questions and limitations
The model learns from what airlines did, not what they would say they prefer
Only flights that changed are observed; those that stayed are not
Every fuel figure is planned fuel, not fuel actually burned
Cases where a better route was never proposed are invisible to this data
A suggestion is only as reliable as the traffic picture it is computed against

## Slide 29: Deployed and serving
01 Registered and version-controlled — MLflow Model Registry, Unity Catalog, on MUAC's Databricks workspace
02 Live REST endpoint — Scores real candidate route sets on request; scales to zero when idle
03 Ready for the next step — A live shadow-mode trial is what would confirm real-world acceptance
The scoring system is live today — the next step is a trial in front of real dispatchers.

## Slide 30: Where the full analysis is documented
SESAR Innovation Days 2026
Presented
Conference-length version
Transportation Research
Part C
In preparation
Full results and limitations

## Slide 31: Questions?
EUROCONTROL Innovation Hub · Maastricht Upper Area Control Centre